## Slide 1
AsymReca
Optical limiter design using 10x less VO2
Asymmetrical resonant cavity thin-film devices designed for VO2 applications
Keywords: optical thin film, thin film design, vanadium dioxide
Unit cell
N
M
1. Introduction
- PCMs change their crystal structure above Ttrans. This greatly alter their n, k index.
- We can use this property to design an optical limiter, optical diode, smart window, optical filter, etc.
- VO2 is a volatile PCM with lowest Ttrans=68°C. It exhibits large mode contrast in the IR spectrum.
- Resonant cavity allows light to cycle the central layer multiple time. Enhance its optical properties while allowing for thinner central layer.
- Resonant cavity can’t be create with PCMs because of their high k index.
- Here, we use an asymmetrical resonant cavity design with VO2 central layer for an optical limiter.
Phase Change Materials
Transition temperature
Vanadium dioxide
Imaginary refractive index
4. Conclusion
- Demonstrated an AsymReca design that allows for precise tuning of VO2’s phase change properties for an efficient optical limiting device.
- Archives similar or better optical performances with significantly reduced Vo2 thickness needed.
- Overall bulkier devices.
- Narrow operation bandwidth limits this design to coherence light.
- High deposition complexity may limit real-world implementation.
Optical Limiter
- Protect human eyes, sensor and laser head.
- Self-activated with high-intensity light.
on
Low power
High power
off
Ex: at 1,550 nm n30°C=2.86+0.28j and n70°C=1.61+2.72j.
3. Result
[5] C. Baratto, et al, “Optical Limiting Sensor Based on Multilayer Optimization of Ag/VO2 Phase Change Material,” IEEE Sensors Letters 7(9).
[6] C. Wan, et al, “Limiting Optical Diodes Enabled by the Phase Transition of Vanadium Dioxide,” ACS Phot. 5(7),
[6] Redesign #1
- Antireflection design
- Resonant @1320 nm
- 14x less VO2 used
2. Theory
- Optical thin film theory: Films thickness determines whether the device exhibits AR or high-reflection property. Normally it’s either QWOT or HWOT.
- Designing resonant cavity: By placing a central layer between two high-reflection mirror will make light bounce through the central layer multiple time. Amplifying the absorption and transmission.
- AsymReca: By using different #N for each side, we can restore resonance with a central PCM layer.
Quarter-wave optical thickness
Half-wave optical thickness
antireflection
[10] A. Sarangan, “Design of resonant cavity thin film structures with complex active layers,” J. Opt. Soc. Am. B 37, 3461-3468 (2020).
References
Chettanat Padungatthakij1, Surawut Wicharn2, and Prathan Buranasiri1*
1Department of Physics, King Mongkut’s Institute of Technology Ladkrabang, 2Advanced Photonic Laboratory, Department of Physics, Faculty of Science, Srinakharinwirot University
*(prathan.bu@kmitl.ac.th)
[1] M. E. A. Warwick, R. Binions, “Advances in thermochromic vanadium dioxide films,” J. Mater. Chem. A 10, 3275-3292 (2014).
[2] Y. Cui, et al, “Thermochromic VO2 for Energy-Efficient Smart Windows,” Joule 2(9), 1707-1746 (2018).
[3] N.R. Mlyuka, G.A. Niklasson, C.G. Granqvist, “Thermochromic multilayer films of VO2 and TiO2 with enhanced transmittance,”
Sol. Energy Mater. Sol. Cells 93(9), 1685-1687 (2009).
[4] M. G. Wood, et al, "Optically-Triggered Optical Limiters for Short-Wavelength Infrared Sensor Protection," 2021 CLEO. 1-2 (2021). https://doi.org/10.1364/CLEO_SI.2021.STh1E.3
[5] C. Baratto, et al, “Optical Limiting Sensor Based on Multilayer Optimization of Ag/VO2 Phase Change Material,” IEEE Sensors Letters 7(9), 1-3 (2023).
[6] C. Wan, et al, “Limiting Optical Diodes Enabled by the Phase Transition of Vanadium Dioxide,” ACS Phot. 5(7), 2688-2692 (2018).
[7] X. Tian, and Z.Y. Li, “An Optically-Triggered Switchable Mid-Infrared Perfect Absorber Based on Phase-Change Material of Vanadium Dioxide,”
[8] D. d. Ceglia, et al, “Tunable Filters for Visible Light Based on Resonant VO2 Planar Thin Films," 22nd ICTON, 1-4 (2020).
[9] E. Strelcov, Y. Lilach, and A. Kolmakov, “Gas Sensor Based on Metal−Insulator Transition in VO2 Nanowire Thermistor,” Nano. Lett. 9(6), 2322-2326 (2009).
[10] A. Sarangan, “Design of resonant cavity thin film structures with complex active layers,” J. Opt. Soc. Am. B 37, 3461-3468 (2020).
[11] M. N. Polyanskiy. “Refractiveindex.info database of optical constants,” Sci. Data 11. 94(2024).
[12] A. Saragan. “Optical Thin Film Design (1st ed.),” CRC Press. (2020).

## Slide 2
on
Low power
High power
off
AsymReca
Optical limiter design using 10x less VO2
Introduction
Sb2Se3 is a non-volatile phase-change material (PCM) with very low absorption in the IR spectrum [1].
Its crystallization temperature is 186 °C, comparable to GST (180 °C) but is lower than other non-volatile PCMs (GSST and Sb2S3) [2].
It has been demonstrated to have high endurance (107 cycles) [2].
In photonics, it’s mainly used as reconfigurable waveguide [3] but can also be used as optical limiter [4].
Asymmetrical design is used to restore resonant in device with imaginary index. [5]
We designed a 1-D thin film device with anti-reflection property for 532 and 1064 nm limiter.

## Slide 3
Design and Simulation of Sb2Se3-Based Asymmetric Resonant Optical Limiters Using Transfer Matrix Method
Keywords: Optical limiter; Asymmetric resonant cavity; Phase change material
    Prathan Buranasiri1, Chettanat Padungatthakij1, Suebtarkul Suchat2, and Surawut Wicharn3*
    1 Department of Physics, School of Science, King Mongkut’s Institute of Technology Ladkrabang;
    2 Department of Physics, Faculty of Science and Technology, Phranakhon Rajabhat University;
    3 Department of Physics, Faculty of Science, Srinakharinwirot University; * Corresponding author Email: surawutw@g.swu.ac.th
References
[1] K. Aryana et al., “Optical and thermal properties of Ge2Sb2Te5, Sb2Se3, and Sb2S3 for reconfigurable photonic devices [Invited],” Optical Materials Express 13, 3277–3286 (2023).
[2] D. Lawson et al., “Optical switching beyond a million cycles of low-loss phase change material Sb2Se3,” Opt. Mater. Express 14(1), 22–38, Optica Publishing Group (2024).
[3] W. Jia, R. Menon, and B. Sensale-Rodriguez, “Unique prospects of phase change material Sb2Se3 for ultra-compact reconfigurable nanophotonic devices,” Opt. Mater. Express 11(9), 3007–3014, Optica Publishing Group (2021).
[4] R. K. Yadav et al., “Giant enhancement of nonlinear absorption in graphene oxide—Sb2Se3 nanowire heterostructure,” Journal of Applied Physics 125(2), 025702 (2019).
[5] A. Sarangan, “Design of resonant cavity thin film structures with complex active layers,” 3461–3468, Optica Publishing Group (2020).
[6] M. Delaney et al., “A New Family of Ultralow Loss Reversible Phase-Change Materials for Photonic Integrated Circuits: Sb2S3 and Sb2Se3,” Advanced Functional Materials 30(36), 2002447 (2020).
3. Result
Refractive indices of amorphous (top) and crystalline (bottom) Sb2Se3. Data is taken from [6].
Resonant cavity diagram. H is high refractive index value material, Si3N4 in this case. L is low-value material SiO2. And C is the central layer, Sb2Se3 in this work.
M and N are the number of unit cell in the incident and substrate side, respectively.
1. Introduction
Sb2Se3 is a non-volatile phase change material (PCM) with very low absorption in the IR spectrum[1]. Its crystallization temperature is 186°C, comparable to GST (180 °C), but is lower than other non-volatile PCMs such as GSST or Sb2S3[2]. Sb2Se3 has been demonstrated to have high phase transition endurance in the order of 107 cycles [2]. These properties make it attractive as a reconfigurable waveguide[3]. But its usage in another photonic device, optical limiter, hasn’t been explored much [4].
Here, we proposed an optical limiter design utilizing asymmetrical resonant cavities comprised of Sb2Se3 as central layer.
2. Theory
Anti-reflection can be achieved by quarter-wave optical thickness.
Resonant cavity allows light to cycle through the central PCM layer(s) multiple times, increasing the total absorptivity.
We use Asymmetrical resonant cavity with different number of unit cell on each side, it’s possible to restore resonance even with high k index material [5].
4. Conclusion
A) 532 nm
To archive perfect antireflection property, asymmetrical design is required. Symmetrical-unit-cell design has the best transmission mode contrast ratio, while asymmetrical design have the best Δ mode contrast.
B) 1064 nm
A half-wave optical thickness film with perfect antireflection property can be achieved. While to archive better mode contrast in a cavity design, the device itself needs to be thicker, (e.g., almost ten times thicker than the original).
A) 532 nm
T: 8% / 1%
R: 30% / 49%
Sb2Se3: 67.1 nm
Device: 67.1 nm
T: 34% / 10%
R: 0% / 2%
Sb2Se3: 38.5 nm
Device: 433.2 nm
T: 50% / 24%
R: 0% / 6%
Sb2Se3: 5.4 nm
Device: 591.9 nm
B) 1064 nm
T: 100% / 29%
R: 0% / 70%
Sb2Se3: 157.9 nm
Device: 157.9 nm
T: 100% / 26%
R: 0% / 72%
Sb2Se3: 105 nm
Device: 1496 nm
N
M